Physical Computing
Date Created January 2021
Reviewed
Version

Description
Physical computing involves interactive systems that can sense and respond to the world around them.

# Introduction
Physical Computing is all about interacting with the world around us using Computer Science. It usually involves monitoring, controlling ans observing.

My favourite example of Physical Computing is demonstrated by the daily shipping forecast.
There are weather stations placed about 40km apart thorough the country these capture weather data every minute, 24 hours a day, seven days a week, every day of the year. The data they need are collected by sensors designed for specific measurements.
Meteorologists look at data and observations, monitor charts and produce forecasts every six hours. They provide weather forecasts for all the waters around the British Isles.
## What is measured?
With few exceptions, the following meteorological elements are measured at all weather stations:
- Air temperature at 1.25 m above the ground
- Air temperature over a grass surface or its artificial equivalent
- Air temperature over a concrete surface
- Soil temperature at 0.1 m, 0.3 m and 1.0 m below the ground level
- Relative humidity at 1.25 m above the ground
- Amount of rainfall
- Depth of lying snow
- Mean wind speed, mean wind direction and maximum gust at 10m above the ground
- Atmospheric pressure at the station level and reduced to mean sea level
- Pressure tendency and characteristic
- Visibility
- Amount of cloud
- Type of cloud identified by observer
- Height of cloud base
- Present and past weather
The measurement of almost all the elements on the list is fully automated; sensor data are logged at the station, processed to convert the measurement to a meteorological element in standard format, and transmitted to a central collecting system (Cray XC40 supercomputer) based at the Met Office's headquarters at Exeter.

## Requirements
To complete the work in this tutorial you will need the following
A Raspberry Pi computer with the Raspberry Pi operating system installed. A power cable, USB keyboard and mouse, an HDMI cable and monitor.
The CamJam LED kit with breadboard, LEDs, Resistors, switch, buzzer and connectors.
The PiStop traffic lights.

Appendix 1

Resistor Colour Codes